## Slide 1: FVID2 Interface
9th March 2017
Version 1.0

## Slide 2: Agenda
Introduction
  Challenges in Defining Video Driver Interface
  What is and what is not FVID2?
FVID to FVID2
  Limitation of FVID
Understanding FVID2
  Interfaces
  Application Flow
  Features supported

## Slide 3: Introduction - Interface definition challenges
Typical problems with conventional video interfaces
  Should provide same look and feel for video applications across different Silicon
  Interface should be independent of OS/Hardware/Driver so that it is scalable
  Common APIs for display, capture and memory operation like scaling – reduces data structure manipulation/copy from one operation to other in different stages of operation in chain
  Video composition- Multi-window Operation – Multiple buffers representing a single frame, say, 16 video streams representing one frame
    Challenge is that same interface should be scalable for 1 video stream as well
  Multi channel capture say 16 D1/64 CIF capture – interface should be capable to take multiple buffers
    Challenge is that same interface should be scalable for 1 video stream as well
  Multiplexed capture - One queue could have multiple dequeue/callback
  All drivers should be non-blocking i.e. display, capture and memory operation
Notes: 3

## Slide 4: Introduction - Interface definition challenges contd..
Typical problems with conventional Memory drivers
  Memory operation should have similar capabilities to take inputs from multiple streams as talked in section for reducing software/driver overheads
    Challenge is that same interface should be scalable for 1 to n video stream at both input and output
  Number of input and output streams differ depending upon memory operations like
    Scalar requires one input and one output
    De-interlace may require 2/3 previous frames i.e. 2/3 input and one output
    Noise filter may require future frame i.e. 2 input and one output
    Two scalar in inline with capability to go back in memory – requires one input and two output
    Challenge is dealing of these variations in the single API
  Video composition in the memory driver
  Sliced based support for low latency application
  Interface should be scalable for OSD/graphics plane
Notes: 4

## Slide 5: Introduction
What is FVID2?
  Next version of FVID and it addresses the different limitations of FVID
  Provides interface to streaming operations like queuing of buffers to driver and getting back a buffer from the driver
  Abstracts the underlying hardware for the video application with a standard set of interface
  Gives a same look and feel for video applications across different SOC
  Interface is independent of OS/Hardware/Driver
  FVID2 is currently supported on DSP/BIOS OS
What is not FVID2?
  Not the actual driver
  Does not define hardware specific APIs and structures

## Slide 6: FVID to FVID2 – Limitation of FVID
Feature | Supported in FVID? | Supported in FVID2?
Non-blocking interface with callback for display/capture/M2M (memory to memory) drivers | No – Even though supported by GIO/SIO of BIOS | Yes
Multi-window Operation – Multiple buffers representing a single frame | No | Yes
Multiplexed capture/M2M drivers – Queue/Dequeue can take multiple requests | No | Yes
Multiplexed capture - One queue could have multiple dequeue/callback | No | Yes
M2M driver interface | No – Supports only stream IO | Yes
Per frame changes like scaling, positioning etc… | Not supported directly – can use the reserved field of FVID Frame structure | Yes
Field based capture/display (in case of de-interlaced display) | No | Yes
Sliced based capture/memory operation | No | Yes

## Slide 7: Understanding FVID2 - Interfaces
FVID2_init
  Initializes the drivers and the hardware. Should be called before calling any of the FVID2 functions
FVID2_deInit
  Un-initializes the drivers and the hardware
FVID2_create
  Opens a instance/channel video driver
FVID2_delete
  Closes a instance/channel of a video driver
FVID2_control
  To send standard (set/get format, alloc/free buffers etc..) or device/driver specific control commands to video driver
FVID2_queue
  Submit a video buffer to video driver. Used in display/capture drivers
FVID2_dequeue
  Get back a video buffer from the video driver. Used in display/capture drivers
FVID2_processFrames
  Submit video buffers to video driver for processing. Used only in M2M drivers

## Slide 8: Understanding FVID2 - Interfaces
FVID2_getProcessedFrames
  Get back the processed video buffers from video driver. Used only in M2M drivers
FVID2_start
  Start video capture or display operation. Not used in M2M drivers
FVID2_stop
  Stop video capture or display operation. Not used in M2M drivers
FVID2_Frame
  Represents the video frame buffer along with other meta data
  This is the entity which is exchanged between driver and application and not the buffer address pointers
  Meta data include timestamp, field ID, per frame configuration, application data etc…
  Since video buffers can have up to 3 planes and two fields (in the case of YUV planar interlaced), buffer addresses are represented using a two dimensional array of pointers of size 2 (field) x 3 (planes)

## Slide 9: Understanding FVID2 - Interfaces
FVID2_Frame – How address pointers are used?
Field 0
Field 1
Y0
U0
V0
Y1
U1
V1
YUV 422/420 Planar Buffer Format (Interlaced)
Field 0
Field 1
YUV 422 Interleaved Buffer Format (Interlaced)
YUYV
YUYV
Field 0
Field 1
YUV 422 Interleaved Buffer Format (Progressive)
YUYV
Field 0
Field 1
RGB888
RGB 888 Packed Buffer Format (Progressive)

## Slide 10: Understanding FVID2 - Interfaces
FVID2_FrameList
  Represents N FVID2_Frame
  N Frames could represent
    Different capture channels in multiplexed capture
    Buffer address for each of the window in multi window mode
  N is fixed at 64 in the current implementation
Frame List
Channel 0 Frame
Channel 1 Frame
Channel 2 Frame
Frame List
Window 0 Frame
Window 1 Frame
Window 2 Frame

## Slide 11: Understanding FVID2 - Interfaces
FVID2_ProcessList
  Represents M FVID2_FrameList for input and output frames
  Each frame list represents a N frame buffers for each of the inputs and outputs in M2M drivers
  Used only in M2M drivers
Process List
Input 0 Frame List
Input 1 Frame List
Input 2 Frame List
Output 1 Frame List
Output 0 Frame List

## Slide 12: Understanding FVID2 – Application Flow 1
FVID2 Create
FVID2 Queue – Prime buffers
Get Callback
FVID2 Queue
Steady State
Open Sequence
FVID2 Delete
Close Sequence
Wait for Callback
Signal Task
Task Context
ISR Context
FVID2 Dequeue
Dequeue is non-blocking!!
Driver Specific Configuration
FVID2 Start
FVID2 Stop
FVID2 Dequeue – Flush Driver Q
Typical Display/Capture Application Flow
Frame Processing
Display – Get a displayed buffer and fill the buffer with next frame data
Capture – Get a captured buffer and give the buffer for processing
Dequeue returns FVID2_EAGIAN if no buffers are available to dequeue

## Slide 13: Understanding FVID2 – M2M Application Flow 1
FVID2 Create
FVID2 Process Frames
Get Callback
Steady State
Open Sequence
FVID2 Delete
Close Sequence
Wait for Callback
Signal Task
Task Context
ISR Context
FVID2 Get Processed Frames
Dequeue is non-blocking!!
Driver Specific Configuration
Typical M2M Application Flow
App Process Frames
Note:
1. Start/stop not needed as the operation starts as soon as a buffer is queued for processing and is returned as soon as a buffer is processed
2. Priming of buffers is not a must in a typical M2M driver as most M2M driver can start processing with one buffer

## Slide 14: Understanding FVID2 – Multiple Frames Per Request Feature
This feature supports
  Multi-window display (Multiple buffers belonging to one stream)
  Multiplexed capture (Multiple buffers belonging to multiple streams)
  Multiple M2M request per call (Multiple request belonging to multiple streams/channels)
FVID2 Frame -> one buffer/request
FVID2 FrameList -> Multiple buffers/requests
FVID2_FrameList contains an array of FVID2_Frame pointers whose size if fixed at 64 in the current implementation
typedef struct FVID2_Frame_t
{
Ptr addr[2][3];
UInt32 channelNum;
/* Other members not shown */
} FVID2_Frame;
typedef struct FVID2_FrameList_t
{
FVID2_Frame *frames[64];
UInt32 numFrames;
/* Other members not shown */
} FVID2_FrameList;
Ptr 1
Ptr 2
Ptr 3
Ptr 4
FVID2 Frame 1
FVID2 Frame 3
FVID2 Frame 2
FVID2 Frame 6
4
Unused
Unused

## Slide 15: Understanding FVID2 – One Q, Multiple DQ
Used in multiplexed capture
  While priming, application submits buffers for all the channels using Queue call
  Since multiplexed inputs could be asynchronous, capture could complete at different time for each of the inputs
  Application wants to process the buffers as soon as they are captured
  Hence they are de-queued immediately without waiting for other channels to complete
  This will result in multiple dequeue for a single queue
Queue buffers for N channels
Capture completes for channels 1, 3, 6
Callback
DeQueue buffers for 3 channels (1, 3, 6)
Capture completes for channels 2, 4
Callback
DeQueue buffers for 2 channels (2, 4)
Application
Driver

## Slide 16: Understanding FVID2 – One Q, Multiple DQ Contd…
How is this achieved?
  Only frames are queued/dequeued in/from the driver
  Frame list is not queued/dequeued
  Frame list acts like a container to submit the frames to the driver in Queue call and take back the frames from the driver in dequeue call
  For queue call, application is free to re-use the same frame list again without dequeuing
  For dequeue call, the application has to provide the frame list to the driver and the driver copies the captured frame to the frame list
FVID2 Queue
Frame List - Filled
Frames
Frame List - Empty
Driver InQ
Frames
Pend Frames
Driver OutQ
Done Frames
Completion
Callback
FVID2 Dequeue
Frame List - Empty
Done Frames
Frame List - Completed

## Slide 17: Understanding FVID2 – M2M Interface
Key M2M Driver Requirements | Covered already by FVID2
Non-blocking | Callbacks supported
Support multiple request per call | Frame List supports this
Support multiple inputs and multiple outputs | Is covered now!!
Hypothetical
M2M
Hardware
N Inputs
M Outputs

## Slide 18: Understanding FVID2 – M2M Interface Contd…
FVID2 FrameList -> Multiple buffers/requests per input/output
FVID2_ProcessList -> Multiple input and multiple output which in turn could contain multiple requests
FVID2_ProcessList contains an array of FVID2_FrameList pointers for both input streams and output streams separately
Two more new APIs – FVID2_processFrames(), FVID2_getProcessedFrames() instead of FVID2_queue(), FVID2_dequeue() which are used for stream drivers (display/capture)
typedef struct FVID2_Frame_t
{
Ptr addr[2][3];
UInt32 channelNum;
/* Other members not shown */
} FVID2_Frame;
typedef struct FVID2_FrameList_t
{
FVID2_Frame *frames[64];
UInt32 numFrames;
/* Other members not shown */
} FVID2_FrameList;
typedef struct FVID2_ProcessList_t
{
FVID2_FrameList *inFrameList[FVID2_MAX_IN_OUT_PROCESS_LISTS];
FVID2_FrameList *outFrameList[FVID2_MAX_IN_OUT_PROCESS_LISTS];
UInt32 numInLists;
UInt32 numOutLists;
} FVID2_ProcessList;
I1 RPtr
1
O1 RPtr
O2 RPtr
2
R1 I1
R2 I1
R3 I1
R1 O1
R2 O1
R3 O1
R1 O2
R2 O2
R3 O2
R1 Ptr
R2 Ptr
R3 Ptr
R1 Ptr
R2 Ptr
R3 Ptr
R1 Ptr
R2 Ptr
R3 Ptr
Frame Lists
Frames
Process List

## Slide 19: Understanding FVID2 – M2M Interface Contd…
Similar to queue/dequeue calls, only frame lists are queued/dequeued in/from the driver
Process list is not queued/dequeued
Now Process list acts like a container
Hence application can’t reuse the submitted frame lists till it gets them back from driver
FVID2 Process Frames
Process List - Filled
Frames
Process List - Empty
Driver InQ
Frames
Pend Frames
Driver OutQ
Done Frames
Completion
Callback
FVID2 Get Processed Frames
Process List - Completed
Frames
Frame List 1
Frame List 2
Frames
Pend Frames
Process List - Empty
Done Frames
Done Frames
Done Frames

## Slide 20: Understanding FVID2 – M2M Interface Contd… Multi-window Mode
Process list -> One M2M request containing multiple frame list for each of the ip/op paths
Frame list -> Has multiple frame pointers for the buffer pointers for each of the request
Multi window mode -> Each frame could contain W windows
Frame pointer could represent only one window
Do we need another dimension/structure/dereferencing to obtain this?
Proposed Solution:
  No need to define another structure
  Frame list will contain the frame pointers for all the windows of all the request

## Slide 21: Understanding FVID2 – M2M Interface Contd… Multi-window Mode
Consider a memory driver which gets video from multiple buffers, composite, scales it and write it back to memory
Assume two channels – 1st uses four windows and 2nd channel uses three
Frame list for the above two request at one call looks like
R1 W1
R1 W2
R1 W3
R1 W4
Hypothetical
M2M
Hardware
W1
W2
W3
W4
Composited R1
Out Buffer
Four buffers representing an input for R1 request
Out Frame List
numFrames = 2 (1+1)
R1 O1
R2 O1
R1 W1
R1 W2
R1 W3
In Frame List
numFrames = 7
(4 + 3)
R1 W4
R2 W1
R2 W2
R2 W3
R1 window frames
R2 window frames

## Slide 22: Understanding FVID2 – M2M Interface Contd… Multi-window Mode
Advantage
  No need extra structure or third dimension or another dereferencing
  Application can reuse the same frame pointer structure from a different driver for the window buffers
Other points
  The order (left to right, top to bottom etc…) of the window buffers in a frame list is not defined by FVID2. The individual drivers can impose the order based on its implementation
  Implicit splitting of window buffers based on configured multi-window mode for each channel (In previous example, 4 and 3 is not passed anywhere in the queue call!!)

## Slide 23: Understanding FVID2 – Slice Based Operation
Used in systems which need low latency video processing
Each frame is split in to N number of equal size slices
Typical low latency application might have 4/8 slices per frame
Application needs to be intimated as soon as a slice is captured or processed

## Slide 24: Understanding FVID2 – Slice Based Operation in M2M drivers
Slice level processing can be enabled for each channel using create time configuration.
Slices can be Queued as they are available using same frame processing API.
Slice information has to be updated for each slice inside ‘FVID2_Frame’ under ‘FVID2_SliceInfo’.
typedef struct
  {
  UInt32 sliceNum;
  /**< Current slice Number in this frame,
  range is from 0 to (NoOfSlicesInFrame-1) */
  UInt32 numSlcInLines;
  /**< Number of lines available in the frame at the end of this slice. */
  UInt32 numSlcOutLines;
  /**< Number of lines generated in output buffer after processing
  current slice */
  } FVID2_SliceInfo;
M2M driver will process the given slice and updates output info for further processing in chain. Simultaneously Capture or Video Decoder may add subsequent slice to the frame.
M2M driver keeps a copy of frame info and works using that to avoid conflict with other driver updating this data.
Slice processing completion call back is similar to Frame based processing.

## Slide 25: Understanding FVID2 – Slice Based Operation in Capture Driver
Uses a separate callback mechanism compared to the FVID2 completion callback
Callback gives reference to the current frame being captured/processed
Slice callback will be called per channel per stream of the driver instance
Prototype of Slice based callback
  typedef Int32 (*FVID2_SliceCbFxn) (FVID2_Handle handle,
  FVID2_Frame *Frame);

## Slide 26: Understanding FVID2 – Error Callback
Queue operations are asynchronous and most probably returns success even though there are some error in the submitted frames
Errors are checked in the FVID2 frames only at the time of processing of the frames – which might occur at a later point of time
Also there could be asynchronous hardware errors
So there should be some mechanism through which errors are returned to the application asynchronously
Hence error callbacks are used

## Slide 27: Understanding FVID2 – Error Callback Contd…
When error occurs driver needs a free container (frame list in case of display/capture drivers or process list in case of M2M drivers) to return the queued buffers back to the application
Hence at the time of channel creation, application gives an empty container to the driver along with application error handler
This container will be used at the time of error callback
Prototype of error callback
typedef Ptr (*FVID2_ErrCbFxn) (FVID2_Handle handle,
Ptr appData,
Ptr errData,
Ptr reserved);
Points to either a frame or process list
Application can return the same container or a different container depending on whether the application empties the container in the error callback or not

## Slide 28: Benefits of new FVID2 interface
It address all concerns/challenges discussed for the existing video driver interface
There is no other interface which allows multi channel capture/ multi window display along with memory operation
This helps in improving performance because
  It does not requires data structure to be populated or modified when application is working in chain as capture -> Noise filter-> Deinterlace->scale->display
  It makes application simpler to be developed and debugged
  It has increased ease of use for API
Notes: 28

## Slide 29: Questions? Thank You